Batched Generation of Block-Jacobi Preconditioners for Iterative Sparse Linear System Solvers on GPUs
Hartwig Anzt, Jack Dongarra, Goran Flegar,
Enrique S. Quintana-Ortí, Andrés E. Tomás
ICCS 2017, Zürich, Switzerland

---
Iterative linear system solvers
- Goal: solve linear system using an iterative Krylov method
- Convergence typically benefits from using a preconditioner
- ILU-type preconditioners offer limited concurrency
source: devblogs.nvidia.com/parallelforall/

---
Iterative linear system solvers
- Goal: solve linear system using an iterative Krylov method
- Convergence typically benefits from using a preconditioner
- ILU-type preconditioners offer limited concurrency
- Need high degree of parallelism to use a GPU effectively
  - ILU on GPUs is an area of active research
source: devblogs.nvidia.com/parallelforall/

---
GPU Architecture (NVIDIA GP100)
- 56 SMs x 64 cores = 3584 cores!
- Need to oversubscribe to hide memory latency!

---
Different Approach
- Scalar Jacobi
  - Scale with inverses of diagonal elements
- Block-Jacobi
  - Scale with inverses of diagonal blocks (possibly of different sizes!)
  - Can reflect the block structure of the problem
  - Often superior to scalar Jacobi
- Can proces each block independently
  - Suitable for GPUs

---
General Ideas
- Restrict block size to 32x32
  - Larger block-sizes require more memory to store the preconditioner
  - More efficient implementation

---
General Ideas
- Restrict block size to 32x32
  - Larger block-sizes require more memory to store the preconditioner
  - More efficient implementation
- Use a single warp to process the whole block
  - No need for explicit synchronization

---
General Ideas
- Restrict block size to 32x32
  - Larger block-sizes require more memory to store the preconditioner
  - More efficient implementation
- Use a single warp to process the whole block
  - No need for explicit synchronization
- Use the large register file to store the entire block
  - Read/write from global memory
  - No load/store instructions
  - Com. via warp shuffles

---
Different options
- Inversion in preconditioner setup + matrix-vector product in application
  - (2n3 + 2n2 FLOPS)
  - H. Anzt et all., “Batched Gauss-Jordan Elimination for Block-Jacobi Preconditioner Generation on GPUs”, PMAM’17
- Matrix decomposition in setup + solve in application
  - (2/3n3 + 2n2 FLOPS)
  - Gauss-Huard decomposition

---
Inversion?!

---
Gauss-Huard decomposition
- Decomposition
  - GEMV (DOT at each thread)
  - GER (AXPY at each thread)
  - Column pivoting
    - Do not swap the columns, just remember which thread holds which column of the result
- Solve
  - Store only the solution vector into registers
  - DOT (reduction)
  - AXPY (map)
  - Store lower part transposed wrp. to anti-diagonal for coalesced mem. access

---
Comparison to batched LU (MAGMA)

---
Application time

---
Total runtime of block-Jacobi preconditioned BiCGSTAB

---
Thank you! Questions?
All functionalities are part of the MAGMA-sparse project.
This research is based on a cooperation between Hartwig Anzt, Jack Dongarra (University of Tennessee),
Goran Flegar, Enrique S. Quintana-Ortí and Adrés E. Tomás (Universidad Jaume I)

---
Colors