Batched Generation of Block-Jacobi Preconditioners for Iterative Sparse Linear System Solvers on GPUs
Hartwig Anzt, Jack Dongarra, Goran Flegar, Enrique S. Quintana-Ortí,
Andrés E. Tomás

---
Problem setting
Solve sparse linear system using an iterative Krylov method

---
Problem setting
- Solve sparse linear system using an iterative Krylov method
- Convergence typically benefits from using a preconditioner

---
Problem setting
- Solve sparse linear system using an iterative Krylov method
- Convergence typically benefits from using a preconditioner
- Conventional ILU-type preconditioners offer limited concurrency
- Need high degree of parallelism to use a GPU effectively
  - ILU on GPUs is an area of active research
source: devblogs.nvidia.com/parallelforall/

---
Problem setting
- Solve sparse linear system using an iterative Krylov method
- Convergence typically benefits from using a preconditioner
- Conventional ILU-type preconditioners offer limited concurrency
- Need high degree of parallelism to use a GPU effectively
  - ILU on GPUs is an area of active research
source: devblogs.nvidia.com/parallelforall/

---
GPU architecture (NVIDIA GP100)
- 56 SMs x 64 cores = 3584 cores!
- Need to oversubscribe to hide memory latency!
source: devblogs.nvidia.com/parallelforall/

---
Different approach
- Scalar Jacobi
  - Scale with inverses of diagonal elements
- Block-Jacobi
  - Scale with inverses of diagonal blocks (possibly of different sizes!)
  - Can reflect the block structure of the problem
  - Often superior to scalar Jacobi
  - Lower convergence rate improvement compared to ILU
- Can proces each block independently!

---
General Ideas
- Restrict block size to 32x32
  - Large block sizes require more memory to store the preconditioner matrix

---
General Ideas
- Restrict block size to 32x32
  - Large block sizes require more memory to store the preconditioner matrix
- Use a single warp to process the whole block (one thread per column)
  - No need for explicit synchronization

---
General Ideas
- Restrict block size to 32x32
  - Large block sizes require more memory to store the preconditioner matrix
- Use a single warp to process the whole block (one thread per column)
  - No need for explicit synchronization
- Use the large register file to store the entire block
  - Read/write from mem. once
  - Avoids load/store instructions
  - Com. via warp shuffles

---
Benefits of block-Jacobi
- 40 matrices from SuiteSparse
- MAGMA-sparse open source library
  - IDR solver
  - Jacobi preconditioner
  - Supervariable blocking
- Block-Jacobi improves the robustness of the solver
  - More problems converge
- Decreases time-to-solution

---
Implementation options
- Inversion in preconditioner setup + matrix-vector product in application
  - (FLOPS: 2n3 setup, 2n2 app.)
  - H. Anzt et all., “Batched Gauss-Jordan Elimination for Block-Jacobi Preconditioner Generation on GPUs”, PMAM’17

---
Different options
- Inversion in preconditioner setup + matrix-vector product in application
  - (FLOPS: 2n3 setup, 2n2 app.)
  - H. Anzt et all., “Batched Gauss-Jordan Elimination for Block-Jacobi Preconditioner Generation on GPUs”, PMAM’17
- Matrix decomposition in setup + solve in application
  - (FLOPS: 2/3n3 setup, 2n2 app.)
  - Gauss-Huard decomposition

---
Inversion?!

---
Gauss-Huard decomposition
- Decomposition
  - GEMV
  - GER
  - Column pivoting
    - Do not swap the columns, just remember which thread holds which column of the result
- Solve
  - Store only the solution vector into registers
  - DOT (reduction)
  - AXPY (map)
  - Store lower part transposed wrp. to anti-diagonal for coalesced mem. access

---
Comparison to batched LU (MAGMA)
Block size 16
Block size 32

---
Application time
1,000,000 unknowns

---
Total runtime of block-Jacobi preconditioned BiCGSTAB

---
Thank you! Questions?
All functionalities are part of the MAGMA-sparse project.
This research is based on a cooperation between Hartwig Anzt, Jack Dongarra (University of Tennessee),
Goran Flegar, Enrique S. Quintana-Ortí and Adrés E. Tomás (Universidad Jaume I)